## Slide 1: Orbit Propagation to Determine Satellite’s Demise
Jacob Bailey
Gus Lee
Michael Lesnewski

## Slide 2: Introduction
Background:
  The Chinese space station Tiangong 1 re-entered the Earths’ atmosphere and fell to its demise on April 2, 2018 over the South Pacific Ocean at 24.5°S 151.1°W.
Project Objective:
  Propagate the orbit of the Tiangong 1 space station and estimate the lifetime of the space station using both numerical integration of the perturbed Keplarian equations of motion and the averaged Gauss’ variational equations.
Source: https://news.sky.com/story/chinese-space-lab-tiangong-1-re-enters-earths-atmosphere-11313548

## Slide 3: Initial Conditions for Orbit Propagation
The initial conditions used for the numerical integration are based on an epoch Julian date of 2458130.58298365 or January 12, 2018.
  Ballistic Coefficient = 1/12.741621/ kg/m²
The lifetime of the space station will be determined when the magnitude of the orbital position vector is less than the equatorial radius of the Earth.

## Slide 4: Orbit Propagation using Keplerian Equations of Motion
The perturbed Keplerian equations of motion are numerically integrated in Python™ using the Runge-Kutta method (RK4).
Equations of Motion:

## Slide 5
Time of a demise: 153 days after the observation epoch or June 14, 2018.
This puts the calculated crash site to be in the North Pacific, about 100 miles northwest of Hawaii.
Calculated Crash Site Location |  | 
Latitude | Longitude | Altitude (km)
35.617 | -176.056 | 7186.99
Final Position (m) | Final Velocity (m/s)
-3762391.12 | 59.76
3577671.24 | -57.18
3704724.90 | -59.06
Results: Numerical Integration of Keplerian Equations

## Slide 6: Plots: Numerical Integration

## Slide 7
The averaged form of Gauss’ variational equations are numerically integrated using Matlab’s ODE45 function.
Equations of Motion:
Orbit Propagation using Gauss’ Variational Equations

## Slide 8: Results: Gauss Variational Equations
Time of a demise: 165 days after the observation epoch or June 27, 2018.

## Slide 9: Plots: Gauss’ Variational Equations

## Slide 10: Conclusion
Both of propagation methods shows consistency with one another in regards to the predicted date of re-entry of the Tiangong 1 (within 2 weeks of each other).
However, the predicted re-entry dates vary from the actual date of re-entry by al most 3 months.
It appears that the drag term reported in the TLE data was significantly underestimating the true drag experienced by the spacecraft.