## Slide 1: Orbit Propagation to Determine Satellite’s Demise
Jacob Bailey
Gus Lee
Michael Lesnewski

## Slide 2: Introduction
Background:
  The Chinese space station Tiangong 1 re-entered the Earth’s atmosphere and fell to its demise on April 2, 2018 over the South Pacific Ocean at 24.5°S 151.1°W.
Project Objective:
  Propagate the orbit of the Tiangong 1 space station and estimate the lifetime of the space station using both numerical integration of the perturbed Keplerian equations of motion and the averaged Gauss’ variational equations.
Source: https://news.sky.com/story/chinese-space-lab-tiangong-1-re-enters-earths-atmosphere-11313548

## Slide 3: Initial Conditions for Orbit Propagation
The initial conditions used for propagation were determined for Julian date 2458130.58298365 or January 12, 2018.
Keplerian Elements at epoch:
  Ballistic Coefficient = 1/12.741621/ kg/m²
The demise of the space station was determined when the magnitude of the orbital position vector was less than the equatorial radius of the Earth for the non-averaged equations and when the perigee radius was less than the equatorial radius for the averaged equations.

## Slide 4: Orbit Propagation using Keplerian Equations of Motion
The perturbed Keplerian equations of motion were numerically integrated in Python™ using the Runge-Kutta method (RK4).
Equations of Motion:

## Slide 5
Time of a demise: 153 days after the observation epoch or June 14, 2018.
  73 day difference from actual re-entry date.
This puts the calculated crash site to be in the North Pacific, about 100 miles northwest of Hawaii.
Calculated Crash Site Location |  | 
Latitude | Longitude | Altitude (km)
35.617 | -176.056 | 7186.99
Final Position (m) | Final Velocity (m/s)
-3762391.12 | 59.76
3577671.24 | -57.18
3704724.90 | -59.06
Results: Numerical Integration of Keplerian Equations

## Slide 6: Plots: Numerical Integration
Altitude and Specific Energy decay as expected due to the presence of drag

## Slide 7
The averaged Gauss variational equations are numerically integrated using Matlab’s ODE45 function.
Equations of Motion:
Orbit Propagation using Gauss’ Variational Equations

## Slide 8: Results: Gauss Variational Equations
Time of a demise: 165 days after the observation epoch or June 27, 2018.
  86 day difference from actual re-entry date.

## Slide 9: Project Conclusions
Both of propagation methods show consistency with one another in regards to the predicted date of re-entry of the Tiangong 1 (within 2 weeks of each other).
However, the predicted re-entry dates vary from the actual date of re-entry by almost 3 months.
It appears that the drag term reported in the TLE data was significantly underestimating the true drag experienced by the spacecraft.
Propagation Method | Date of Re-entry
Perturbed Keplerian Eqs. | June 14, 2018
Gauss’ Variational Eqs. | June 27, 2018